## Slide 1: A robust fetal ECG detection method for abdominal recordings
Marta Stefanelli – 84393A
S. M. M. Martens, C. Rabotti, M. Mischi and R. J. Sluijter, A robust fetal ECG detection method for abdominal recordings, Physiological Measurement, 28, 373, 2007

## Slide 2: The dataset
1 of 10
Set-A from Physionet.org, all the plot are related to a14.
1. ECG signals
Duration = 1 min
Fs = 1000 Hz
2. QRS annotation
It is composed of a sequence of numbers that correspond to the positions, in milliseconds, of the true FQRS peaks.

## Slide 3: The paper
Baseline wander removal
Power line interference canceller
Upsampling
MQRS detection
MECG canceller
FQRS detection
FECG deteciton
2 of 10

## Slide 4: 1. Baseline wander removal
3 of 10
S1 -> S2
Cause: movement and respiration of the patient.
Solution: FIR high-pass filter with a cut-off frequency at 3 Hz.

## Slide 5: 2. Power line interference canceller
4 of 10
S2 -> S3
Cause: disturbance of the electric current.
Solution: adaptive noise cancellation using harmonic frequences of the fundamental frequency 50 Hz.

## Slide 6: 3. Upsampling
5 of 10
S3 -> S4
Done by using the scipy.signal.resample function.

## Slide 7: 4. MQRS detection
6 of 10
S4 transformation
PCA firs component (pca_firs_component)
MQRS template (build_qrs_template)
Cross correlation (detect_qrs_corsscorr)

## Slide 8: 5. MECG canceller
7 of 10
S4 -> S5
10 preceding maternal heartbeats
Different scale factors
Subtraction between the signal and the estimate mother ECG

## Slide 9: 6. FQRS detection
8 of 10
S5 transformation
 | FQRS detection | MQRS detection
High-pass cutoff | 4 Hz | 1 Hz
Percentile | 96 | 98
Refractory | 0.12 s | 0.28 s
Refinement | 15 ms | 20 ms

## Slide 10: 6. FQRS detection
8 of 10
S5 transformation
Mean R-R Interval: 470.73 ms
Estimated Fetal Heart Rate (FHR): 127.46 BPM

## Slide 11: 7. FECG detection
9 of 10
S5 -> S6
Nav = 150 => SNR increase by a factor of = 12

## Slide 12: Performance metrics and results
10 of 10
FQRS detection performances
Signal S1
Signal S5

## Slide 13: Performance metrics and results
10 of 10
Sensitivity | FHR Reliability | F1 | Accuracy
40,62196 | 55,493% | 0,64572 | 55,744%
FQRS detection mean performances

## Slide 14: Thank you
Marta Stefanelli – 84393A